## Slide 1
Chapter 19
Network Layer:
Logical Addressing
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
19-1 IPv4 ADDRESSES
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example, a computer or a router) to the Internet.
Address Space
Notations
Classful Addressing
Classless Addressing
Network Address Translation (NAT)
Topics discussed in this section:

## Slide 3
An IPv4 address is 32 bits long.
Note

## Slide 4
The IPv4 addresses are unique
and universal.
Note

## Slide 5
The address space of IPv4 is
232 or 4,294,967,296.
Note

## Slide 6
Figure 19.1 Dotted-decimal notation and binary notation for an IPv4 address

## Slide 7
Numbering systems are reviewed in Appendix B.
Note

## Slide 8
Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example 19.1
Solution
We replace each group of 8 bits with its equivalent decimal number (see Appendix B) and add dots for separation.

## Slide 9
Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example 19.2
Solution
We replace each decimal number with its binary equivalent (see Appendix B).

## Slide 10
Find the error, if any, in the following IPv4 addresses.
Example 19.3
Solution
a. There must be no leading zero (045).
b. There can be no more than four numbers.
c. Each number needs to be less than or equal to 255.
d. A mixture of binary notation and dotted-decimal
notation is not allowed.

## Slide 11
In classful addressing, the address space is divided into five classes:
A, B, C, D, and E.
Note

## Slide 12
Figure 19.2 Finding the classes in binary and dotted-decimal notation

## Slide 13
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 19.4
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C
address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 14
Table 19.1 Number of blocks and block size in classful IPv4 addressing

## Slide 15
In classful addressing, a large part of the available addresses were wasted.
Note

## Slide 16
Table 19.2 Default masks for classful addressing

## Slide 17
Classful addressing, which is almost obsolete, is replaced with classless addressing.
Note

## Slide 18
Figure 19.3 shows a block of addresses, in both binary and dotted-decimal notation, granted to a small business that needs 16 addresses.
We can see that the restrictions are applied to this block. The addresses are contiguous. The number of addresses is a power of 2 (16 = 24), and the first address is divisible by 16. The first address, when converted to a decimal number, is 3,440,387,360, which when divided by 16 results in 215,024,210.
Example 19.5

## Slide 19
Figure 19.3 A block of 16 addresses granted to a small organization

## Slide 20
In IPv4 addressing, a block of
addresses can be defined as
x.y.z.t /n
in which x.y.z.t defines one of the addresses and the /n defines the mask.
Note

## Slide 21
The first address in the block can be found by setting the rightmost
32 − n bits to 0s.
Note

## Slide 22
A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or
205.16.37.32.
This is actually the block shown in Figure 19.3.
Example 19.6

## Slide 23
The last address in the block can be found by setting the rightmost
32 − n bits to 1s.
Note

## Slide 24
Find the last address for the block in Example 19.6.
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111
or
205.16.37.47
This is actually the block shown in Figure 19.3.
Example 19.7

## Slide 25
The number of addresses in the block can be found by using the formula
232−n.
Note

## Slide 26
Find the number of addresses in Example 19.6.
Example 19.8
Solution
The value of n is 28, which means that number
of addresses is 2 32−28 or 16.

## Slide 27
Another way to find the first address, the last address, and the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number. This is particularly useful when we are writing a program to find these pieces of information. In Example 19.5 the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).
Find
a. The first address
b. The last address
c. The number of addresses.
Example 19.9

## Slide 28
Solution
a. The first address can be found by ANDing the given
addresses with the mask. ANDing here is done bit by
bit. The result of ANDing 2 bits is 1 if both bits are 1s;
the result is 0 otherwise.
Example 19.9 (continued)

## Slide 29
b. The last address can be found by ORing the given
addresses with the complement of the mask. ORing
here is done bit by bit. The result of ORing 2 bits is 0 if
both bits are 0s; the result is 1 otherwise. The
complement of a number is found by changing each 1
to 0 and each 0 to 1.
Example 19.9 (continued)

## Slide 30
c. The number of addresses can be found by
complementing the mask, interpreting it as a decimal
number, and adding 1 to it.
Example 19.9 (continued)

## Slide 31
Figure 19.4 A network configuration for the block 205.16.37.32/28

## Slide 32
The first address in a block is
normally not assigned to any device;
it is used as the network address that represents the organization
to the rest of the world.
Note

## Slide 33
Figure 19.5 Two levels of hierarchy in an IPv4 address

## Slide 34
Figure 19.6 A frame in a character-oriented protocol

## Slide 35
Each address in the block can be considered as a two-level
hierarchical structure:
the leftmost n bits (prefix) define
the network;
the rightmost 32 − n bits define
the host.
Note

## Slide 36
Figure 19.7 Configuration and addresses in a subnetted network

## Slide 37
Figure 19.8 Three-level hierarchy in an IPv4 address

## Slide 38
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
a. The first group has 64 customers; each needs 256
addresses.
b. The second group has 128 customers; each needs 128
addresses.
c. The third group has 128 customers; each needs 64
addresses.
Design the subblocks and find out how many addresses are still available after these allocations.
Example 19.10

## Slide 39
Solution
Figure 19.9 shows the situation.
Example 19.10 (continued)
Group 1
For this group, each customer needs 256 addresses. This means that 8 (log2 256) bits are needed to define each host. The prefix length is then 32 − 8 = 24. The addresses are

## Slide 40
Example 19.10 (continued)
Group 2
For this group, each customer needs 128 addresses. This means that 7 (log2 128) bits are needed to define each host. The prefix length is then 32 − 7 = 25. The addresses are

## Slide 41
Example 19.10 (continued)
Group 3
For this group, each customer needs 64 addresses. This means that 6 (log264) bits are needed to each host. The prefix length is then 32 − 6 = 26. The addresses are
Number of granted addresses to the ISP: 65,536
Number of allocated addresses by the ISP: 40,960
Number of available addresses: 24,576

## Slide 42
Figure 19.9 An example of address allocation and distribution by an ISP

## Slide 43
Table 19.3 Addresses for private networks

## Slide 44
Figure 19.10 A NAT implementation

## Slide 45
Figure 19.11 Addresses in a NAT

## Slide 46
Figure 19.12 NAT address translation

## Slide 47
Table 19.4 Five-column translation table

## Slide 48
Figure 19.13 An ISP and NAT

## Slide 49
19-2 IPv6 ADDRESSES
Despite all short-term solutions, address depletion is still a long-term problem for the Internet. This and other problems in the IP protocol itself have been the motivation for IPv6.
Structure
Address Space
Topics discussed in this section:

## Slide 50
An IPv6 address is 128 bits long.
Note

## Slide 51
Figure 19.14 IPv6 address in binary and hexadecimal colon notation

## Slide 52
Figure 19.15 Abbreviated IPv6 addresses

## Slide 53
Expand the address 0:15::1:12:1213 to its original.
Example 19.11
Solution
We first need to align the left side of the double colon to the left of the original pattern and the right side of the double colon to the right of the original pattern to find how many 0s we need to replace the double colon.
This means that the original address is.

## Slide 54
Table 19.5 Type prefixes for IPv6 addresses

## Slide 55
Table 19.5 Type prefixes for IPv6 addresses (continued)

## Slide 56
Figure 19.16 Prefixes for provider-based unicast address

## Slide 57
Figure 19.17 Multicast address in IPv6

## Slide 58
Figure 19.18 Reserved addresses in IPv6

## Slide 59
Figure 19.19 Local addresses in IPv6